## Slide 2
Procedure call frame:
Hold values passed to a
procedure as arguments
Save registers
Space for local variables

## Slide 3
0 zero constant 0
1 at reserved for assembler
2 v0 expression evaluation &
3 v1 function results
4 a0 arguments
5 a1
6 a2
7 a3
8 t0 temporary: caller saves
. . .
15 t7
MIPS: Software conventions for Registers
16 s0 callee saves
. . .
23 s7
24 t8 temporary (cont’d)
25 t9
26 k0 reserved for OS kernel
27 k1
28 gp Pointer to global area
29 sp Stack pointer
30 fp frame pointer
31 ra Return Address

## Slide 4
Caller:
Pass arguments:
  - First 4 in registers $a0 - $a3;
  - Remaining pushed on the stack (at the beginning of the stack frame)
Save caller-saved registers ($a0-$a3, $t0, $t9). The callee can use these registers.
Execute jal
Callee (before starts running):
Allocate memory for the frame by subtracting the frame size from the stack pointer.
Save callee-saved registers in the frame ($s0-$s7, $fp, $ra) before altering them.
Establish the frame pointer by adding the frame size minus 4 to $sp and storing the sum in $fp.
Callee (before returning):
If it is a function, place the returned value in register $v0
Restore the callee-save registers
Pop the stack frame by subtracting the frame size from $sp
Return by executing jr $ra

## Slide 5
MIPS Calling Conventions
FP
SP
fact:
subu $sp, $sp, 32
sw $ra, 20($sp)
sw $fp, 16($sp)
addu $fp, $sp, 32
sw $a0, 0($fp)
...
lw $ra, 20($sp)
lw $fp, 16($sp)
addu $sp, $sp, 32
jr $ra
ra
old FP
ra
old FP
ra
FP
SP
ra
FP
SP
First four arguments passed in registers.